## Slide 1: Industrializing Broadcast-Quality Streaming
Adam Bedwell
VP – CTO/Sales Engineering - Americas

## Slide 2: All Content And All Screens Are Not Equal
Are the expectations the same?

## Slide 3: Conventional Broadcast vs OTT Latency
Example latencies with 6-second segments
3x 6
0.5
2
4
4
0.5
2
4
6
6
10
Time after live edge
Live edge
at event
TV
OTT
Social
Media
Cable encode
Broadcaster encode
Program distrib.
Contribution
Packaging
CDN
Client
Write and post

## Slide 4: Industry Initiatives to Improve Latency
MP4 file media container
Divides each segment into smaller fragments, but stays one-file-per-segment
HTTP/1.1 Chunked Transfer Encoding to deliver fragments when available
DASH CMAF Low-Latency
MP4 or TS media container
Divides each segment into smaller discrete "part" files, each transferred separately
HTTP/2 push mode required for low latency
Frequent updates to manifest
Multiple manifest permutations depending on the URL request
HLS Low-Latency Extensions
Both can eliminate some of the latency, as long as fully implemented end-to-end
Neither removes the need for the client to have a significant buffer for rate
detection and adaptation

## Slide 5: DASH Fragmentation & Chunked Transfer
Use HTTP/1.1 chunked transfer to move data as soon as available
Full-segment processing
With Fragments and CTE
In theory, could be 1 picture per fragment, but this leads to very small transfer sizes
and doesn't materially help vs (say) 8-frame chunks, because the reordering buffer is still needed
Chunked transfer, or the use of part files, makes measuring download rate more inaccurate

## Slide 6: What about Scalability & Quality
2.6M
98.2M
2019 Superbowl
Viewer Numbers
Streaming needs to scale up massively
more like 100x in terms of delivered bit rate
Client buffering/rate adaptation isn't acceptable
The real need is:
Consistently high quality
Scale
Low latency
All three are needed simultaneously
Viewers
~ 40x
Bit Rate
~ 3x
Typical Bit
Rate Comparison
Broadcast
Streaming

## Slide 7: Multicast For Scalability
Multicast sender & proxy, as per CableLabs MABR
Request segment
Real-time flow
of segments
Multicast push
at media rate
Home
Network
CDN node
ABR client
ABR client
CDN node
Multicast
server
Multicast
Proxy
Conventional
Unicast
ABR system
Multicast
ABR system

## Slide 8: Latency is Impaired
3x 6
0.5
2
4
4
0.5
2
4
6
6
10
Time after live edge
Live edge
at event
TV
OTT +
MABR
Social
Media
Cable encode
Broadcaster encode
Program Distribution
Contribution
Packaging
CDN
Client
Write and post
6
Additional MABR Latency

## Slide 9: Multicast-native into the Client
Use a native multicast mechanism
Eliminates the large client buffer
Multicast scalability
Only fall back to OTT-mechanisms when multicast not available
ALC+LCT (used by 5G mobile & others) provides a good starting point
  Send fragments
  Rates managed by the network
  Flow controlled to guarantee delivery
ABR – but with multicast scale and delivery guarantees
Where scale, quality & latency matter
Clients can use any of:
  Conventional ABR (OTT)
  Multicast proxy
  Multicast native
Maximum client reach
Where reach matters most

## Slide 10: Match the tech to the need.
Meet expectations, for every screen type
Multicast low latency ABR
OTT wide-reach ABR